## Slide 1
PROJECT REVIEW · JUNE 24 - JULY 6, 2026
ZERO
An offline conversational voice companion say a wake word once, then just talk. It listens, thinks, sees, remembers, and replies in a natural human voice.
99 commits in 13 days
Working end to end
Raspberry Pi 5 + GPU node
Private by design — no cloud
Notes: ZERO is an offline voice companion built on a Raspberry Pi 5 paired with a GPU node. In 13 days and 99 commits it went from prototype to a working end-to-end system. Nothing touches the cloud — all traffic stays on a private tunnel.

## Slide 2
What ZERO can do today
Free-flowing conversation
Wake once (“Hey Jarvis”), then talk naturally. It bows out on “goodbye” and can be interrupted mid-reply.
A human-sounding voice
Streamed speech with laughs, sighs and emphasis the first words arrive in about a second.
Sight
An always-on camera loop perceives the room continuously, with grounded distance and bearing no invented scenes.
Memory and presence
Remembers people and facts across sessions, greets by time of day, and makes ambient remarks on its own.
Notes: Four capabilities shipped: natural multi-turn conversation, an expressive streamed voice, always-on grounded vision, and persistent memory with proactive behavior — greetings, ambient remarks.

## Slide 3
Thin client, remote muscle
Raspberry Pi 5 the face
Mic · wake word · speech detection · camera
memory (SQLite) · Bluetooth speaker
SSH tunnel over Tailscale
GPU node - the muscle
Whisper large-v3-turbo - hearing
Gemma 8B via Ollama - thinking
Orpheus, quantized - speaking
Depth Anything V2 - seeing
Fails soft
If the GPU is unreachable, the Pi falls back to small local models and keeps working voice-only, never a crash.
Swappable by design
Every stage sits behind an interface chosen in config.yaml. Moving a model between the Pi and the GPU is a setting change, not a rewrite.
Notes: The Pi handles everything you touch — mic, wake word, camera, memory, speaker. The GPU runs the four heavy models. They talk over a private SSH tunnel on Tailscale, so it works from anywhere with nothing exposed to the internet. Two design wins: graceful fallback to local models, and every engine swappable from config.

## Slide 4
The numbers
SPEECH TO TEXT
~1s
was 29 s on the Pi alone
FIRST TOKEN
~0.6s
Gemma 8B on the GPU
FIRST SPOKEN AUDIO
~1s
streamed as it generates
VISION
10/s
detections, near real time
Transcription time per clip (seconds)
Chart: 
| Pi alone (phase 1) | Pi + GPU tunnel (now)
Seconds | 29 | 1
Replies stream sentence by sentence - ZERO starts speaking before it has finished thinking.
Notes: The headline number: moving speech-to-text to the GPU took a clip from 29 seconds to about 1. First LLM token in 0.6 s, first spoken audio in about a second because speech streams while the reply is still being generated. Vision runs at roughly 10 detections per second.

## Slide 5
The journey in five acts
1
Everything on the Pi
The whole pipeline on the Pi's CPU. Rough, but it proved the concept.
2
Making it usable
Transcription 15 s to 1.5 s; one-shot Q&A became flowing conversation with memory.
3
The wall, the pivot
Heavy models moved to a GPU over SSH; 29 s transcriptions became about 1 s.
4
Making it human
A natural streamed voice, a personality, and emotion cues it can perform.
5
Eyes and presence
Grounded vision, face enrolment, proactive remarks - and it works from anywhere.
Notes: Five acts. One: the proof-of-concept ran entirely on the Pi. Two: made usable — faster transcription, real conversation, SQLite memory. Three: the Pi hit its ceiling, so heavy models moved to a GPU over SSH. Four: a natural streamed voice and a personality. Five: grounded vision, face enrolment, proactivity, and a hardened tunnel that works off-LAN.

## Slide 6
What's next
Switch on voice ID
Already written - ZERO answers only the people it knows.
Finish barge-in
Any speech interrupts it, not just the wake word.
Survive reboots
systemd on both boxes; zero manual steps at startup.
The living-companion roadmap
Identity, agentic tools, human-like memory, self-directed learning.
Full detail in docs/PLAN.md · docs/PROGRESS.md · docs/OPERATIONS.md
Notes: Three near-term items: flip on voice ID (the code exists), finish barge-in so any speech interrupts, and systemd persistence so both boxes boot hands-free. Beyond that, the PLAN.md roadmap: identity, agentic tool use, human-like memory, and self-directed learning — from voice box to living companion.